XIAMEN GOODCOM TECHNOLOGY CO., LTD.

GT81Pro

The portable Android POS Terminal can be used in variety of market applications, such as food takeaway/delivery service, parking, hotel, taxi, lottery, bus tickets, bill payment, mobile airtime top-up/ recharge, mobile payment (deposit & withdraw), online shopping, etc.

Specification

| Hardware/software /Mechanical | Items | Description |
| --- | --- | --- |
|  | CPU | Qualcomm Quad-Core Cortex™-A53 1.3GHz, 64Bit |
|  | GPU | Qualcomm Adreno™ 308 485MHz |
|  | RAM | 2GB LPDDR3 |
| GF | FLASH | 16GB eMMC |
|  | OS | Android 10.0 |
|  | Display | 6 inch color screen |
|  | Touch screen | Multipoint capacitive touch screen |
|  | Keyboard | Power key,Volume key |
|  | WIFI | 2.4G (802.11b/g/n) 5G (802.11ac) |
|  | Bluetooth | BT 4.2 LE |
|  | GNSS | GPS: 1575.42MHz±1.023MHz GLONASS: 1597.5MHz~1605.8MHz BeiDou: 1561.098MHz±2.046MHz |
|  | Camera (optional) | 5 Mega-pixel |
|  | Wireless | 2G: GSM/GPRS/EDGE 3G: WCDMA 4G: LTE-FDD/TDD |
|  | Battery | 7.4V/2600mAh |
|  | USB | USB 2.0, USB OTG |
|  | External memory card | TF card |
|  | Magnetic Card (optional) | Protocol: ISO 7811/7813 Speed: 10cm/sec ~ 150cm/sec Head Life: 800 thousand times |
|  | SmartCard (optional) | Protocol: ISO 7816 Supported Card Type: CPU Card(Bank) |
|  | NFC (optional) | Protocol: ISO 14443A Read Distance: 5cm Supported Card Type: Mifare S50 Mifare S70, Mifare Ultralight CPU Card(Bank) |
|  | Dimensions | 225mm*87mm*58mm |
|  | Module NA (Optional) | 3G: Three-Band UMTS/HSDPA/HSPA+ : B2/B4/B5 |
|  |  | 4G: 12-Band LTE-FDD: B2/B4/B5/B7/B12/B13/B14/B17/ B25/B26/B66/B71 1-Band LTE-TDD: B41 |
|  | Module EM (optional) | 2G: GSM/GPRS/EDGE: B2/B3/B5/B8 |
|  |  | 3G: 5-Band UMTS/HSDPA/HSPA+: B1/B2/B4/B5/B8 |
|  |  | 4G: 9-Band LTE-FDD: B1/B2/B3/B4/B5/B7/B8/B20/B28 4-Band LTE-TDD: B38/B39/B40/B41 |
| Application environment | Operating temperature | -15℃～55℃ |
|  | Relative humidity | 10%~95% |
|  | Environment noise | ≤60dB(A) |
|  | Atmospheric pressure | 86~106kPa |
|  | Frequency stability | <2.5ppm |
|  | Receiver sensitivity | <-104dBm |
|  | GSM protocol | ETSI GSM Phase 2+ |
|  | Transmit power | <2W(GSM, EGSM), <1W(DCS,PCS) |
| GSM parameters | SIM card interface | 1.8V/2.95V Dual SIM cards |
|  | Antenna | Internal,50Ω impedance,3dB gain |
| Power supply | AC input voltage | 100V~240V AC 50/60Hz |
|  | Power adapter output | DC 9V/3A |
| Micro Printer | Printing method | Thermal-line dot method |
|  | Paper | Thermal roll paper (standard) 57*45 mm |
|  | Effective Printing area | 48mm |
|  | Speed | Maximum 70mm/sec(480 dot line/sec) |
|  | Printing resolutions | 8 dots/mm |
|  | Character | 12*24dots and 24*48 dots |
|  | Number of columns | 32columns/line |
|  | Printing head life | Pulse resistance:100 million pulses/dot (under our standard conditions); Abrasion resistance: paper traveling distance 50km (print ratio:25% or less) |